## Slide 1
PROJECT PRESENTATION
EMBEDDED DATA LOGGER
Real-time temperature & humidity monitoring with local data storage
Presented by: Tharun. A
Department: ECE – Final Year
Institution: ______________________________
ESP32 • DHT22 • OLED • microSD

## Slide 2
EMBEDDED DATA LOGGER
Problem Statement & Proposed Solution
ESP32 • DHT22 • OLED • microSD
02
THE PROBLEM
Manual measurement of environmental conditions takes time and may miss important changes. Without a record of readings, it is difficult to review trends, compare conditions, or identify unusual temperature and humidity levels.
THE SOLUTION
Build an ESP32-based embedded data logger that reads temperature and humidity from a DHT22 sensor, shows live values on an OLED display, and saves timestamped readings to a microSD card for later analysis.
Core idea: sense → display → timestamp → store

## Slide 3
EMBEDDED DATA LOGGER
Project Objectives
ESP32 • DHT22 • OLED • microSD
03
01
Measure
Read ambient temperature and relative humidity using the DHT22 sensor.
02
Display
Show current readings and time on a compact OLED screen.
03
Record
Save readings to a microSD card for offline review.
04
Timestamp
Attach date/time information to recorded measurements.
05
Demonstrate
Validate the system through simulation and serial output.

## Slide 4
EMBEDDED DATA LOGGER
System Block Diagram
ESP32 • DHT22 • OLED • microSD
04
DHT22 SENSOR
Temperature + humidity
ESP32
Read, process, control
OLED DISPLAY
Live values + time
microSD CARD
Log file storage
RTC / TIME
Timestamp source
Power supplied to all modules as required by their voltage specifications.
DHT22 SENSOR
Temperature + relative humidity
ESP32 CONTROLLER
Reads, processes, formats and logs data
OLED (SSD1306)
I²C: SDA 21, SCL 22
microSD MODULE
SPI: CS 5, SCK 18, MISO 19, MOSI 23
TIME SOURCE
System / NTP* Timestamp
*Timestamp accuracy depends on the code's configured clock/time synchronization.

## Slide 5
EMBEDDED DATA LOGGER
Components Used
ESP32 • DHT22 • OLED • microSD
05
ESP32 development board
Main controller; reads the sensor and manages display and storage.
DHT22 sensor
Measures ambient temperature and relative humidity.
OLED display (SSD1306)
Displays current readings and status using I²C.
MicroSD card module
Stores logged readings in a file for later analysis.
MicroSD card
Provides removable storage for recorded data.
Connecting wires + USB supply
Provide signal connections and power.
Software libraries
WiFi, DHT, Adafruit SSD1306/GFX, SPI and SD libraries.
Note: the supplied code includes Wi-Fi/time-related libraries; actual time synchronization depends on the configured time source.
ESP32 development board
Main controller; processes sensor data and coordinates peripherals.
DHT22 sensor
Measures ambient temperature and relative humidity. Data pin: GPIO 15.
OLED display (SSD1306)
Displays readings and time over I²C. SDA 21, SCL 22.
microSD module + card
Stores readings; SPI pins CS 5, SCK 18, MISO 19, MOSI 23.
Component visuals are cropped from the supplied Wokwi simulation screenshot.

## Slide 6
EMBEDDED DATA LOGGER
Project Implementation
ESP32 • DHT22 • OLED • microSD
06
1
01 Hardware wiring
Connect DHT22 data to ESP32 GPIO 15. Connect OLED through I²C (SDA 21, SCL 22). Connect microSD through SPI (CS 5, SCK 18, MISO 19, MOSI 23).
2
02 Library setup
Include the Wi-Fi, DHT, SPI, SD, Adafruit GFX/SSD1306 and time libraries in the project.
3
03 Initialization
Start serial output, initialize the sensor and OLED, mount the SD card, and prepare the logging file.
4
04 Sampling loop
Read sensor values, obtain a timestamp, update the OLED and append the reading to the SD log.
The wiring and pin definitions should match the actual circuit before running on physical hardware.
1
01 Wiring
DHT22 data → GPIO 15. OLED I²C → SDA 21 and SCL 22. microSD SPI → CS 5, SCK 18, MISO 19 and MOSI 23.
2
02 Libraries
Use the libraries present in the sketch: WiFi, time, DHT, SPI, SD, Adafruit GFX and Adafruit SSD1306.
3
03 Initialization
Start Serial, initialize the DHT22 and OLED, initialize SPI and mount the SD card. Handle initialization failures.
4
04 Logging loop
Read sensor values, get the current timestamp, update the OLED/serial output, then append the data to microSD.

## Slide 7
EMBEDDED DATA LOGGER
Control Logic / Working Flow
ESP32 • DHT22 • OLED • microSD
07
START
Power on the ESP32
INITIALIZE
Start DHT22, OLED, SPI and SD
READ
Sample temperature and humidity
FORMAT
Add timestamp and format values
DISPLAY
Update OLED with current values
SAVE
Append record to microSD
REPEAT
Wait for the logging interval
Error handling should check sensor validity and SD-card availability before saving each record.
START
Power on ESP32
INITIALIZE
Start DHT22, OLED, SPI and SD
READ
Read temperature and humidity
CHECK
Validate sensor values / SD status
TIMESTAMP
Get time from configured clock source
OUTPUT
Refresh OLED and serial monitor
SAVE + REPEAT
Write record to microSD; wait and repeat
Recommended: show an error message if the sensor read or SD-card write fails.

## Slide 8
EMBEDDED DATA LOGGER
Simulation Output
ESP32 • DHT22 • OLED • microSD
08
Observed in the provided simulation: temperature and humidity readings are printed, and the console reports that data was saved to microSD.
Simulation shows live temperature/humidity output and the message “Data saved to MicroSD.”

## Slide 9
EMBEDDED DATA LOGGER
Advantages
ESP32 • DHT22 • OLED • microSD
09
Automated logging
Reduces repeated manual measurements.
Live monitoring
Values are visible on the OLED display.
Local storage
Data can be reviewed without an internet connection.
Compact design
ESP32 combines processing and connectivity in one board.
Expandable platform
Can be adapted for many indoor monitoring applications.
Low-cost prototype
Uses widely available modules and open-source libraries.

## Slide 10
EMBEDDED DATA LOGGER
Future Scope
ESP32 • DHT22 • OLED • microSD
10
• Add a real-time clock (RTC) module or robust NTP synchronization for accurate timestamps.
• Upload logs to a cloud dashboard using Wi-Fi and MQTT/HTTP.
• Add threshold alerts for high temperature or humidity.
• Create charts and reports from CSV log files.
• Improve reliability with sensor-error checks, SD-card checks and power-loss recovery.
• Use a battery and deep-sleep mode for portable, energy-efficient monitoring.
Possible applications: laboratories, greenhouses, storage rooms, classrooms and equipment enclosures.

## Slide 11
EMBEDDED DATA LOGGER
Conclusion
ESP32 • DHT22 • OLED • microSD
11
The Embedded Data Logger demonstrates how a microcontroller can collect, display and store environmental data automatically.
SENSE
DHT22 measures temperature and humidity.
DISPLAY
OLED presents current values clearly.
STORE
microSD keeps a local record for later review.
Overall, the prototype provides a practical foundation for environmental monitoring and can be enhanced with connectivity, alerts and more robust timekeeping.

## Slide 12
✓
THANK YOU
Questions & Discussion
EMBEDDED DATA LOGGER • ESP32 + DHT22 + OLED + microSD